Feeder Protection From Over Load

Abstract

A busbar in electrical power distribution refers to thick strips of copper or aluminum that conduct electricity within a switchboard, distribution board, substation, or other electrical apparatus.  In this project busbar can be protected from the over current condition. Industrial instruments failures have many causes and one of the main causes is over load.   The primary of the distribution transformer or any other transformer is designed to operate at certain specific current, if that current flowing through that instrument is more than the rated current, then immediately the System may burn because of over load, through this project we are going to protect the busbar from over load condition. In this project work for generating high current more loads are applied to the circuit; so that the current will be increased. When ever the over current occurred the circuit will be tripped. To trip the circuit we are using one relay which will control through our microcontroller. When over load is occurred relay will trip the total circuit and buzzer will on to indicate over load.

For protection of bus bar from over current condition first we have to measure the total load current which is flowing through the busbar. Here we are using CT for measuring the load current and the output of CT is given to ADC for converting analog output of CT into digital data. That ADC output is given to microcontroller for monitoring purpose. When current are increases certain limit then we are going to trip the load by using relay. In this project we are using 230v bulbs as a load. We are going to increase the load by increasing the number of bulbs ON. When we ON more bulbs it causes over load condition and microcontroller will detect that and it will trip the total load by using relay. In this project we are using 230v, 7 amp relay for tripping purpose. Here we are using LCD for displaying the total load current which is flowing in the circuit.

Block Diagram:

HARDWARE COMPONENTS:

- Microcontroller

- Power supply

- Relays

- LCD

- Loads

- ADC Inbuilt

- Current Transformer

SOFTWARE TOOLS:

- PICC Compiler

- ExpressSCH

- Embedded C

- Express PCB

Applications:

- This project is used for protecting Bus bars in sub stations, generating stations etc.

- Used for Industrial appliances protection

# Text boxes

MICROCONTROLLER

Power

Supply

Current sensor

RELAY

FEEDER Supply

Load

Buzzer

L

C

D

ADC