Android Smart Phone operated Weighing Machine

The project aims in designing a system which makes operating of Digital Thermal printers  in Shops through Android mobile phone possible. The controlling of Weighting  machineis done wirelessly through Android smart phone using the Bluetooth feature present in it. Here in this project the Android smart phone is used as a remote control for operating the Digital thermal printer.

Android is a software stack for mobile devices that includes an operating system, middleware and key applications. Android boasts a healthy array of connectivity options, including Wi-Fi, Bluetooth, and wireless data over a cellular connection (for example, GPRS, EDGE (Enhanced Data rates for GSM Evolution), and 3G). Android provides access to a wide range of useful libraries and tools that can be used to build rich applications. In addition, Android includes a full set of tools that have been built from the ground up alongside the platform providing developers with high productivity and deep insight into their applications.

Bluetooth is an open standard specification for a radio frequency (RF)-based, short-range connectivity technology that promises to change the face of computing and wireless communication. It is designed to be an inexpensive, wireless networking system for all classes of portable devices, such as laptops, PDAs (personal digital assistants), and mobile phones. It also will enable wireless connections for desktop computers, making connections between monitors, printers, keyboards, and the CPU cable-free.

The controlling device of the whole system is a Microcontroller. Bluetooth module, Load sensor  and LCD display are interfaced to the Microcontroller. The data received From Microcontroller and transmitted over the  Bluetooth module To  Android smart phone. The controller acts accordingly to   measure the weightage and display on the lcd . Also, the status of the Weighting  machine can be seen on LCD display. In achieving the task the controller is loaded with a program written using Embedded ‘C’ language.

The main objectives of the project are:

- Controlling of AC devices wirelessly through mobile phone.

- Usage of Android touchscreen smart phone in performing the task.

- Bluetooth wireless transmission.

- Display of Weighting  machine status on Lcd display.

The project provides exposure to following technologies:

- Google’s Android Open Source Technology.

- Bluetooth wireless technology.

- Interfacing Bluetooth module to Microcontroller.

- Interfacing of Load sensor module to Microcontroller.

- Embedded C programming.

- PCB designing.

The major building blocks of the project are:

- Regulated Power Supply.

- Microcontroller.

- Bluetooth module.

- Load sensor module

- LCD display with driver.

- Crystal oscillator.

- Reset.

- LED indicators.

- Weighting  machine.

Software used:

- PIC-C compiler for Embedded C programming.

- PIC kit 2 programmer for dumping code into Micro controller.

- Express SCH for Circuit design.

Regulated Power Supply:

Block diagram: