Solar fencing to prevent crop damage by animals

The project aims at developing a solar fencing, which helps farmers to avoid their crop damage usually occur due to animals. Solar energy is used to power up the fence through shock generation circuitry. The system has a provision for ON/OFF the solar fence according to farmers wish.

Electric fences can be used to protect farmhouses, farmlands, forest bungalows, etc from animals.  In a way, these simulate the job of a cowboy or forest guard. Already popular in countries where manpower is expensive, electric fences are slowly becoming popular in India as well. These control the animals by giving them a short, sharp but safe shock that teaches them to stay away from the fence. Thus electric fences are economical and practical solutions to maximize field production through controlled grazing.

The project makes use of a solar plate. The solar energy obtained is stored to a battery. The battery supply is fed to pulse generator and in turn to a MOSFET which is capable of generating ON/OFF pulses of different frequencies. This is fed to a step up transformer to generate a low voltage AC. This AC is fed to electrical fence, which will give shock when any animal comes in contact with it.

Future Scope: This project can be extended in a way such that the output from the solar plate is increased. This can be done by increasing the dimensions of the solar plate.

Conclusion: The project concludes a design of “Solar fencing to prevent crop damage by animals” such that the fencing to the crops or fields from solar plate generates solar energy and utilizing this energy for fencing system.

The objectives of the project:

- Storing solar energy.

- Creating shocking circuitry.

- ON/ OFF control for fence.

The project focuses on the following areas:

- Pulse generation techniques.

- Solar cell working principle.

- MOSFET working principle.

The major building blocks of this project are:

- Solar panel.

- Pulse generator.

- MOSFET.

- Step up transformer.

- ON/ OFF switch.

- Fence.

Block Diagram: