AUTOMATIC POWER FACTOR CORRECTOR USING CAPACITIVE LOAD BANK

This project provides continuous power factor correction without manual capacitive bank loading. A PFC controller provides power factor correction and peak current limiting for a switch-mode power converter of any topology (buck, boost or buck-boost), without having to directly sense inductor current. The PFC control technique involves using a piecewise-polynomial analog computer (AC) to compute power transistor on-times in accordance with separate polynomial transfer functions for power-factor control and peak-current-linking using as inputs current representations of line input voltage (VLN), load output voltage (VLD), and long-term current demand (VCD). A conduction cycle is initiated by sensing when the rate of change in the inductor current reaches zero using an auxiliary winding on the current storage inductor, and terminated after the computed on-time to implement either power-factor control or peak-current-limiting.

The Reactive Power charge on your electricity bill is directly targeted against those companies who do not demonstrate clear energy efficiency use. You will find this charge itemized on electricity bill. Reactive power charges can be made significantly smaller by the introduction of Power Factor Correction Capacitors which is a widely recognized method of reducing an electrical load and minimizing wasted energy, improving the efficiency of a plant and reducing the electricity bill.  It is not always necessary to reach a power factor of 1. A cost effective solution can be achieved by increasing your power factor to greater than 0.95

This project uses regulated 5V, 750mA power supply. 7805 three terminal voltage regulator is used for voltage regulation. Bridge type full wave rectifier is used to rectify the ac out put of secondary of 230/12V step down transformer.

This project provides us with the learning’s on the following aspects:

- Embedded C programming.

- PCB Design concepts.

- Zero-crossing detector interfacing with Microcontroller.

- Current transformer interfacing.

- Potential transformer interfacing.

The major building blocks of this project are:

- Regulated Power Supply.

- Microcontroller.

- Resistive load.

- Inductive load.

- Relay bank unit.

- Current transformer.

- Potential transformer.

- Zero-crossing detector.

- LCD display.

- LED indicators.

Software used:

- PIC-C compiler for Embedded C programming.

- PIC kit 2 programmer for dumping code into Micro controller.

- Express SCH for Circuit design.

- Proteus for hardware simulation.

Regulated Power Supply:

Block diagram:

# Text boxes

Power supply to all sections

Step down T/F

Bridge Rectifier

Filter Circuit

Regulator