Solar Inverter using super capacitor

The project aims at developing a solar inverter, which helps farmers to control devices like irrigation water pump, fencing etc. Solar energy is used to power up the battery. The system has a provision for ON/OFF the solar battery charging according to farmers wish.

The project makes use of a solar plate. The solar energy obtained is stored to a battery. The battery supply is fed to pulse generator and in turn to a MOSFET which is capable of generating ON/OFF pulses of different frequencies. This is fed to a step up transformer to generate a low voltage AC. This AC is fed to loads like water pump, devices. The system also uses super capacitor to increase the battery life.

Future Scope: This project can be extended in a way such that the output from the solar plate is increased. This can be done by increasing the dimensions of the solar plate.

Conclusion: The project concludes a design of “Solar based inverter” such that the inverter was designed and from solar plate generates solar energy and utilizing this energy for load.

The objectives of the project:

- Storing solar energy.

- Design of inverter.

- ON/ OFF control for loads.

The project focuses on the following areas:

- Pulse generation techniques.

- Solar cell working principle.

- MOSFET working principle.

The major building blocks of this project are:

- Solar panel.

- Pulse generator.

- MOSFET.

- Step up transformer.

- ON/ OFF switch.

- Super capacitor

- Rechargeable battery

Block Diagram: