Wireless 3-phase motor starter using Bluetooth with Android

Voice Feedback and SMS alerts

The main aim of this project is controlling of 3-phase motor using wireless technology based on Bluetooth. The project was designed in such a way that user can easily switch ON/OFF the 3-phase motor at distance of Bluetooth module range.

In this project we are using Android and Bluetooth app which will communicate with Bluetooth module connected to Microcontroller. This microcontroller also interfaced with two electro-magnetic relays which are used to control 3-phase Starter’s ON OFF buttons. We use micro controller at the receiver end, which is programmed to control the output modules depends on the input.  We have feed-back indicators using Voice and LED Indicators and also with SMS alerts. For remote SMS alerts we are using GSM modem interfaced with same Microcontroller above.

The Microcontroller is programmed using Embedded C language.

The main objectives of this project are:

- Interfacing of Bluetooth Module.

- Interfacing of GSM modem.

- Interfacing of Relays with Microcontroller.

The learning’s provided by the project are:

- Wireless Bluetooth Communication.

- Conversion of AC supply to DC supply.

- Characteristics relay and starter.

- GSM communication.

- Interfacing of relays with starter (any three phase starter).

- Embedded C programming.

- PCB design concepts.

The major building blocks of this project are:

- Regulated Power Supply.

- Microcontroller.

- Crystal oscillator.

- Android app based Control buttons.

- Bluetooth Module.

- GSM Modem

- Reset Button.

- Relays with drivers.

- LED Indicators.

Software used:

- PIC-C compiler for Embedded C programming.

- PIC kit 2 programmer for dumping code into Micro controller.

- Express SCH for Circuit design.

Regulated Power Supply:

Block diagram: