Construction of Cooking gas leakage sensor and alarming system without using Microcontroller

The project aims in designing a system which is capable of sensing gas leakages and alerts regarding the leakages using buzzer. Also, the system has a provision for changing the intensity of gas leakages.

The system makes use of a comparator. The output from gas sensor is fed to

Comparator. The comparator will continuously compare output from gas sensor and reference voltage and generates logic low or high. The output generated from comparator is used to drive a Buzzer.

The major features of this project are:

- Automated gas sensing alerting system.

- Alerts the buzzer when gas detects

- Intensity of gas leakage can be adjusted.

The project provides learning’s on the following advancements:

- Characteristics of gas sensor.

- Conversion of AC supply to DC supply.

- Comparator working principle.

- PCB design.

The major building blocks of this project are:

- Regulated Power Supply.

- Comparator.

- Gas sensor.

- Buzzer with driver.

- Reference voltage (Potentiometer).

Advantages:

- Alerting the peoples who work in dangerous gas leakages areas.

- Alerts through buzzer alarm system.

- Efficient low cost design.

- Low power consumption.

Disadvantages:

- Interfacing of sensor module is sensitive.

- Gas sensor sensing is moderate.

Applications:

This system can be practically in real time anywhere like in chemical industries, packing materials, identification of sensitive materials like wires in any explosives etc.., where security is most concerned.

Regulated Power Supply:

Block Diagram: